## Slide 1: Fair Path Planning for Unmanned Aerial Vehicles (UAVs) in Emergency Response Missions
Germán Pardo González
Camilo Gómez
Carlos Francisco Rodríguez

## Slide 2: Agenda
Motivation
Mathematical models
  Objectives
  Column Generation approach
  Q-Learning approach
Computational experiments
Conclusions and future work

## Slide 3: Reinforcement Learning in Cyber-Physical Systems
Juan Betancourt Osorio, Germán Pardo González, Samuel Rodriguez Gonzalez, Daniel Cuellar, Camilo Gómez, Francesco Mariotti, Leonardo Montecchi, and Paolo Lollini. 2023. Modeling attacker behavior in Cyber-Physical-Systems. In Proceedings of the 11th Latin-American Symposium on Dependable Computing (LADC '22). Association for Computing Machinery, New York, NY, USA, 117–124. https://doi.org/10.1145/3569902.3570188
Modelled attacker agent using a universal optimisation framework
The solution algorithms were Q-Learning and Value Iteration as a benchmark

## Slide 4: Ethical dilemmas in autonomous vehicles
If an autonomous vehicle (AV) loses its brakes at , what should the car do?
Awad, E., Dsouza, S., Kim, R. et al. The Moral Machine experiment. Nature 563, 59–64 (2018). https://doi.org/10.1038/s41586-018-0637-6

## Slide 5: Fatality risk probability
Logistic regression to model probability of fatality
Works to quantify reward function depending on the philosophic theory
Jin Nie, Guibing Li & Jikuang Yang (2015) A Study of Fatality Risk and Head Dynamic Response of Cyclist and Pedestrian Based on Passenger Car Accident Data Analysis and Simulations, Traffic Injury Prevention, 16:1, 76-83, DOI: 10.1080/15389588.2014.881477

## Slide 6: New context inspiration: UAV deployment in emergency response
Path planning using 4 different heuristics to maximise node coverage within a grid network in emergency response scenarios using UAVs
A. Anastasiou, P. Kolios, C. Panayiotou and K. Papadaki, "Swarm Path Planning for the Deployment of Drones in Emergency Response Missions," 2020 International Conference on Unmanned Aircraft Systems (ICUAS), Athens, Greece, 2020, pp. 456-465, doi: 10.1109/ICUAS48674.2020.9213876.

## Slide 7: Fair navigation planning in autonomous robots
Unfairness against population coverage
Works to choose a Pareto-optimal solution between the population covered and unfairness in the initial routing planning for the drones
Martim Brandão, Marina Jirotka, Helena Webb, Paul Luff, Fair navigation planning: A resource for characterizing and designing fairness in mobile robots, Artificial Intelligence, Volume 282, 2020, 103259, ISSN 0004-3702, https://doi.org/10.1016/j.artint.2020.103259.

## Slide 8: Ethics in autonomous systems?
Etzioni, A., Etzioni, O. Incorporating Ethics into Artificial Intelligence. J Ethics 21, 403–418 (2017). https://doi.org/10.1007/s10892-017-9252-2

## Slide 9: Millions of possible routes: perfect for the Column Generation method
Iterative method that provides an attractive route based on the reduced costs of the auxiliary problem (AP)
Easily connected to Pulse algorithm to dramatically accelerate subproblem’s computation time
Leonardo Lozano, Daniel Duque, Andrés L. Medaglia (2015) An Exact Algorithm for the Elementary Shortest Path Problem with Resource Constraints. Transportation Science 50(1):348-357.https://doi.org/10.1287/trsc.2014.0582
Feillet, D. A tutorial on column generation and branch-and-price for vehicle routing problems. 4OR-Q J Oper Res 8, 407–424 (2010). https://doi.org/10.1007/s10288-010-0130-z

## Slide 10: Agenda
Motivation
Mathematical models
  Objectives
  Column Generation approach
  Q-Learning approach
Computational experiments
Conclusions and future work

## Slide 11: Fair routes planning
Maximise population coverage in the initial routing while ensuring fairness in a considerable amount of computation time

## Slide 12: Who should the UAVs prioritise and why?
Maximise population coverage in the initial routing while ensuring fairness in a considerable amount of computation time
Tackle ethical dilemmas based on survival probability, battery time and medical resource constraints

## Slide 13: Agenda
Mathematical models
  Objectives
  Column Generation approach
  Q-Learning approach

## Slide 14: Solution scheme

## Slide 15: Nomenclature
Sets
Locations to visit. {1, 2, …, n}
Feasible routes.
Graph:

## Slide 16: Nomenclature
Parameters for the master problem
Some parameters are defined conveniently:
cost of entering node
price of the route .
number of UAVs available

## Slide 17: Master Problem defined as the knapsack problem
Every node is traversed at most one time
Maximum number of UAVs
Variables definitions

## Slide 18: Relaxed Master Problem
Consists on relaxing the binary constraints
We retrieve the dual variables to compute the reduced costs in every iteration

## Slide 19: Nomenclature
Parameters for the auxiliary problem
Altered costs:
cost of entering node
probability of vulnerability of arc
dual variables from MP
weights for each objective
battery time for each UAV

## Slide 20: AP defined as the longest-path with resource constraints problem
Flow constraints
Resource constraint
Subtours constraints
Variables definitions

## Slide 21: Column Generation procedure
Feillet, D. A tutorial on column generation and branch-and-price for vehicle routing problems. 4OR-Q J Oper Res 8, 407–424 (2010). https://doi.org/10.1007/s10288-010-0130-z
Fig 1. Column Generation pseudo-code

## Slide 22: Column Generation enhancement with warm-start
A. Anastasiou, P. Kolios, C. Panayiotou and K. Papadaki, "Swarm Path Planning for the Deployment of Drones in Emergency Response Missions," 2020 International Conference on Unmanned Aircraft Systems (ICUAS), Athens, Greece, 2020, pp. 456-465, doi: 10.1109/ICUAS48674.2020.9213876.
Fig 2. Greedy Best heuristic pseudo-code

## Slide 23: Pareto front procedure
George Mavrotas, Effective implementation of the ε-constraint method in Multi-Objective Mathematical Programming problems, Applied Mathematics and Computation, Volume 213, Issue 2, 2009, Pages 455-465, ISSN 0096-3003, https://doi.org/10.1016/j.amc.2009.03.037.
Optimisation |  | 
 | 35 | 8,37
 | 5 | 16,26
Optimisation |  | 
 | 35 | 8,37
 | 5 | 16,26
Where and
Table 1. Payoff table for both objectives

## Slide 24: Pareto front procedure
Being δ a step, and is the minimum value for . This is a process of reoptimising every time the parameter ϵ is updated on each iteration.
Now, with the payoff table computed, the optimisation problem to build the Pareto front consisted of making one of the objectives as a constraint, Equations (2.2)-(2.11) formulate the iterative process to compute the Pareto front.
Where β is a small number between and , SV is a slack variable, r is the range of and ϵ is calculated each iteration by:

## Slide 25: Agenda
Mathematical models
  Objectives
  Column Generation approach
  Q-Learning approach
Notes: Geohash

## Slide 26
Framework for Stochastic Optimisation
Notes: Es parecido a un MDP pero sirve para otros approaches

## Slide 27
State space for the problem
Where
position of the drone in the -axis
position of the drone in the -axis
available resource of the drone
takes the value of 1 if the survivor has already been visited
Notes: Es parecido a un MDP pero sirve para otros approaches

## Slide 28
Available drone’s actions
Where
move in the -axis
move in the -axis
assign resource
Notes: Es parecido a un MDP pero sirve para otros approaches

## Slide 29
Uncertainty in the number of survivors
Number of survivors in a given node
Notes: Es parecido a un MDP pero sirve para otros approaches

## Slide 30
Rewards and penalties for the agent
  Move penalty: -5
  Station reward: 200
  Battery penalty: -300
  Survivor already visited: -n
  Survivor visit: n
Notes: Es parecido a un MDP pero sirve para otros approaches

## Slide 31
Reinforcement Learning Algorithm
Exploration on the environment and exploitation of recollected information
Estimation of a Q-table which is updated on every episode
Q-Learning algorithm
Notes: Model free algorithm this means that the agent doesnt need to know the set of parameters but trough exploration it Will learn from the env.

## Slide 32: Agenda
Motivation
Mathematical models
  Objectives
  Nomenclature
  Parameters
  Column Generation approach
  Q-Learning approach
Computational experiments
Conclusions and future work
Notes: GUIOON

## Slide 33: Pareto front for a small instance and instance generation
The instance has been generated conveniently so the fairness is away from the depot and the population is nearer the depot

## Slide 34: Initial solution provided by heuristic

## Slide 35: Optimising on population coverage

## Slide 36: Optimising on mid-point

## Slide 37: Optimising on fairness

## Slide 38: Computation time comparison with the new Elementary Shortest Path Problem With Resource Constraints (ESPPRC)
All the results were run in processor Intel(R) Core (TM) i5-8250U CPU @ 1.60GHz 1.80 GHz, RAM 8,00 GB (7,86 GB usable) in type 64-bit operating system, x64-based processor in Gurobi optimiser under version 10,0 and academic license

## Slide 39: Parameters
Hyper-parameters for the Reinforcement Learning model
140
100 (battery level)
0,9
0,9998
0,1
0,95

## Slide 40
Learning curve of q-learning
Notes: Es parecido a un MDP pero sirve para otros approaches

## Slide 41: Agenda
Motivation
Mathematical models
  Objectives
  Nomenclature
  Parameters
  Column Generation approach
  Q-Learning approach
Computational experiments
Conclusions and future work

## Slide 42
The Column Generation approach using a warm start shows an improvement throughout the iterations
We showed a trade-off between fairness and population in an emergency response situation
Conclusions

## Slide 43
Properly quantify fairness and include metrics to compare the results depending on the metric
Accelerate the Auxiliary Problem using the Pulse algorithm and adding more feasible and attractive routes
Future Work

## Slide 44
https://copa.uniandes.edu.co/
Questions?
gr.pardo@uniandes.edu.co